## Slide 1: IoT @ FMI Lection 5
22.03.2017

## Slide 2: Power Consumption
ESP8266 (2.9-4.2v)
  Active: 30-300 ma
  Sleep: 0.1 – 10 ma
Arduino (Atmega328p)
  Active: 4-20 ma
  Sleep: 0.001 – 0.01 ma
Raspberry PI
  Active: 80-240 ma
BLE/Zigbee modules
  0.02ma (BLE), 0.05ma (Zigbee)

## Slide 3: Types of Batteries
Type | Voltage (V) | Capacity (mAh) | Resistance | Self Discharge
Coin Cell 2032 | 3.00 | 200 | High | Low
AAA/AA/C/D (Alkaline) | 1.2 – 1.5 | 1000/2000/5000/10000 | Medium | Low
AAA/AA/C/D (NiMh) | 0.2 – 1.3 | same | Medium | Med/Low
AAA/AA/C/D (Ni-Zn) | 1.3 – 1.6 | Same | > | ?
LiPo (Generic) | 3.3 – 4.2 (3.7) | 10 – 5000 | Low | Low
LiPo - 16850 | Same | 1000 – 5000 |  | 
LiPo – 14500 | Same | 500 – 1000 | Low | Low

## Slide 4: Battery Discharge Curve
Internal Resistance increases with decreased capacity
1 om @ 300 ma = 0.3v voltage Drop

## Slide 5: ESP8266 – DeepSleep
Sleep current in DeepSleep is 0.08 ma
Connect D0 and RST with a jumper wire
Call ESP.deepSleep(time); delay(1000);
ESP will go to deep sleep and reset after “time”
Time is in us (1,000,000 us = 1,000 ms = 1 sec)
RTC Memory can be used to store data between iterations
After wake up it takes ~300 ms to boot and ~3-10 sec to connect to WiFi
All GPIOs are set to INPUT during sleep
http://www.espressif.com/sites/default/files/9b-esp8266-low_power_solutions_en_0.pdf

## Slide 6: ESP8266 – LIGHT and MODEM sleep
Modem Sleep: ~15 ma. Just use delay(xxx)
Light Sleep: ~0.5 ma
  Details: https://github.com/esp8266/Arduino/issues/1381#issuecomment-279117473

## Slide 7: LiPo Chargers
+ battery protection
Only Charge
Wemos Battery Shield
  + battery protection
  + 5v Boost

## Slide 8: Popular Software

## Slide 9: NodeRED
Design flows
Java Script
Dashboards

## Slide 11: Thingspeak
Easy integration
Lots of display options

## Slide 12: Blynk – Arduino to Mobile

## Slide 13: Ubidots – IoT Dashboards

## Slide 14: BeeBotte

## Slide 15: Popular Hardware

## Slide 16: Sonoff
https://www.itead.cc/search/result/?cat=&q=sonoff

## Slide 17: Broadlink

## Slide 18: Grove / Wio Link

## Slide 19: Xiaomi